## Slide 1: Development of an Open-Source Cosimulation Method of the Knee
Anne Schmitz and Davide Piovesan

## Slide 2: Abnormal kinematics after soft tissue injury can drastically affects the aging process.
5 degrees
http://www.manordrug.com/FLA/kneeguide.htm
Andriacchi et al, 2006
44%

## Slide 3
Abnormal Kinematics (from ACL Injury or Reconstruction) Cause Shifts in Cartilage Loading
High weight bearing cartilage
Thicker
More randomly oriented collagen fibers
Low weight bearing cartilage
Thinner
More orderly oriented collagen fibers
Compression
Tension
Normal Cartilage
Compression
Tension
Fluid flows to other regions
Tearing of collagen fibers
Left picture:
Li, Moses et al. 2006
Right picture:
Andriacchi, Briant et al. 2006
Adapted from (Chaudhari, Briant et al. 2008)
Adapted from (Chaudhari, Briant et al. 2008)

## Slide 4: Estimation of Internal Knee Loads (Fernandez et al, 2006)
Muscle Forces
Multibody Dynamics
1 DOF joint that behaves independent of load (Arnold et al, 2010)
Detailed Joint Model
Ligament Stress and Strain
Cartilage Stress and Strain
Secondary Joint Kinematics
Boundary
Conditions
Serial Approach
Cosimulation Approach
Goal: How is cartilage load affected by simulation approach?
Notes: Important field of study in biomechanics

## Slide 5: Serial approach was initially used to calculate cartilage contact loads during a simple knee flexion motion.
Muscle Forces
Multibody Dynamics
1 DOF joint that behaves independent of load (gait 2392 model Arnold et al. 2010)
OpenSim software used
Computed muscle control (Thelen and Anderson 2006) used to calculate muscle forces needed to track a right knee flexion angle from 0 – 50 degrees
Ligament Forces
Cartilage Forces
Secondary Joint Kinematics
Detailed Joint Model
7 DOF joint with ligaments and contact (Schmitz and Piovesan, 2016)
Free to download https://simtk.org/home/kneemodel/
Muscle forces used to actuate model via forward dynamics simulation

## Slide 6: Cosimulation approach was then used to calculate cartilage contact loads during a simple knee flexion motion.
Muscle Forces
Multibody Dynamics
1 DOF knee joint replaced with detailed joint model
Free to download https://simtk.org/home/uwcosim
Computed muscle control (Thelen and Anderson 2006) used to calculate muscle forces needed to track a right knee flexion angle from 0 – 50 degrees
Ligament Forces
Cartilage Forces
Secondary Joint Kinematics

## Slide 7: Computed Muscle Control Algorithm
Thelen et al, 2006
PD Controller:
Compute the desired accelerations needed to drive the model coordinates to the given experimental coordinates
Experimental motion

## Slide 8: Computed Muscle Control Algorithm
Thelen et al, 2006
PD Controller:
Compute the desired accelerations needed to drive the model coordinates to the given experimental coordinates
Experimental motion
Static Optimization:
Compute the actuator controls x (e.g. muscle excitations/forces, idealized joint moments) that will achieve the desired accelerations
Muscle excitations and forces
Cj = 0

## Slide 9: Computed Muscle Control Algorithm
Forward Dynamics:
Integrate forward in time to calculate new model states
Thelen et al, 2006
PD Controller:
Compute the desired accelerations needed to drive the model coordinates to the given experimental coordinates
Experimental motion
Static Optimization:
Compute the actuator controls x (e.g. muscle excitations/forces, idealized joint moments) that will achieve the desired accelerations
Muscle excitations and forces

## Slide 10: Serial method predicted lower muscle force and cartilage contact load.
Add some pics

## Slide 11: Why?
Serial approach assumed more posterior tibia
Decrease moment arm of the flexors
Increase moment arm of the extensors
Increase in force to maintain torque
Decrease in force to maintain torque

## Slide 12: Take Home Message
Important factors affecting calculation of soft tissue loads:
  Choice of method to calculate muscle forces
  Translational degrees of freedom
1 dof knee model underestimates cartilage loading
Cosimulation approach free to download at https://simtk.org/home/uwcosim

## Slide 13: Thank You
Gannon Faculty Research Grant
Gannon Faculty Release Time
Gannon Faculty Development Grant