## Slide 1: Cosimulation of Soft Tissue Loads and Multibody Dynamics
Anne Schmitz

## Slide 2: Introduction
2 approaches used in the literature to estimate soft tissue loads
  Serial
  Cosimulation
Serial approach assumes kinematic joints that behave independent of load
As a consequence, this impacts the muscle moment arms and ultimately the calculated muscle forces
Muscle forces are the main contributor to cartilage contact loads, a key clinical variable in the development of osteoarthritis
Goal of study: Investigate how serial versus cosimulation approaches affect cartilage contact loads

## Slide 3: Methods
Use gait2392 model scaled to Runner18 (motion capture data collected from Schmitz’s post-doc at UK)
Detailed joint model already established
  https://simtk.org/home/kneemodel/
Detailed joint model incorporated into scaled gait2392 model
Estimate cartilage contact loads during a simple knee flexion movement
  Serial
  Cosimulation with CMC of the detailed joint model
  Use the open-source software OpenSim
    https://simtk.org/projects/opensim

## Slide 4: Serial approach was initially used to calculate cartilage contact loads during a simple knee flexion motion.
Muscle Forces
Multibody Dynamics
1 DOF joint that behaves independent of load (gait 2392 model Arnold et al. 2010)
OpenSim software used
Computed muscle control (Thelen and Anderson 2006) used to calculate muscle forces needed to track a right knee flexion angle from 0 – 50 degrees
Ligament Forces
Cartilage Forces
Secondary Joint Kinematics
Detailed Joint Model
7 DOF joint with ligaments and contact (Schmitz and Piovesan, 2016)
Free to download https://simtk.org/home/kneemodel/
Muscle forces used to actuate model via forward dynamics simulation

## Slide 5: First Step of Serial Approach
Use scaled gait2392 model with a hinge knee joint
Perform:
  Inverse dynamics
  Static optimization
  Computed muscle control
Perform these analyses by running Model -> Hinge -> run_CMC.cmd
Muscle Forces
Ligament Forces
Cartilage Forces
Secondary Joint Kinematics

## Slide 6: When assuming a hinge knee joint, CMC adequately tracks knee flexion (0-50 deg) with little torque from the reserve actuator. Nearly all of the torque needed to drive the motion comes from the muscles.
Good point: no problem with passive tendon forces

## Slide 7: Second Step of Serial Approach
Use muscle activations (output from CMC on hinge joint) to drive detailed model of knee
Perform:
  Forward dynamics
Perform this analyses by running Model -> Serial -> run_CMC.cmd
Muscle Forces
Ligament Forces
Cartilage Forces
Secondary Joint Kinematics

## Slide 8: When a serial approach is used, secondary kinematics are not consistent with those assumed in the hinge joint when muscle forces were calculated. These secondary kinematics may alter muscle moment arms, which may in turn affect estimates of muscle forces and ultimately cartilage contact loads.

## Slide 9: Cosimulation approach was then used to calculate cartilage contact loads during a simple knee flexion motion.
Muscle Forces
Multibody Dynamics
1 DOF knee joint replaced with detailed joint model
Free to download https://simtk.org/home/uwcosim
Computed muscle control (Thelen and Anderson 2006) used to calculate muscle forces needed to track a right knee flexion angle from 0 – 50 degrees
Ligament Forces
Cartilage Forces
Secondary Joint Kinematics

## Slide 10: Cosimulation of a Simple Motion
All dof locked except for knee
1 dof patellofemoral joint
6 dof tibiofemoral joint
Track time-varying knee flexion using computed muscle control
Perform:
  Computed muscle control
  Inverse dynamics (to compare joint torques with CMC reserve actuators)
Perform these analyses by running Model -> Simple_Motion5 -> run_CMC.cmd

## Slide 11: When joint laxity is included in the estimation of muscle forces, CMC adequately tracks the prescribed kinematics. The non-zero reserve actuator torque is due to passive structures since CMC cannot account for this in the optimization algorithm.

## Slide 12: By assuming a kinematic joint, the serial simulation under predicts the total muscle force during the movement. Hence, the cartilage contact loads are also underestimated.